## Slide 1: RISC-V Out-Of-Order Processor with Tomasulo’s Algorithm
By: Antonio Anzora Jr
ECE 622 – Digital Systems Structure
Notes: Hi my name is Antonio. This presentation covers my implementation of a RISC-V out-of-order processor using Tomasulo’s Algorithm in VHDL

## Slide 2: Agenda
Motivation
Tomasulo’s Algorithm Overview
System Architecture & Key Components
Simulation Results

## Slide 3: Motivation – Why out of order?
In-order execution wastes cycles waiting for dependencies
Modern CPUs execute 3-4 instructions per cycle
Out-of-order allows instructions to execute based on data availability
Reduces cycle time compared to in-order approaches
Notes: Let me explain why out-of-order execution matters.
In-order execution wastes cycles waiting for dependencies.
Imagine you have three instructions. Instruction 1 adds two numbers and stores the result in register x1. Instruction 2 needs that result — it can't execute until instruction 1 finishes. So instruction 2 stalls and waits.
Meanwhile, instruction 3 doesn't depend on anything. It's ready to go right now. But in an in-order processor, instruction 3 has to wait behind instruction 2. It sits idle. That's wasted processing power.
Modern CPUs execute 3-4 instructions per cycle.
That means the processor has multiple execution units working in parallel. An ALU, a memory unit, maybe more. They can all work at the same time. But if we're waiting for dependencies, we're not using all that hardware. We're leaving performance on the table.
Out-of-order execution allows instructions to execute based on data availability.
Instead of waiting for program order, we execute whichever instruction is ready. If instruction 3 has its operands ready, it goes now. Don't wait for instruction 2.
This reduces cycle time.
More instructions finish per cycle. Faster performance. That's why modern CPUs use it.

## Slide 4: Tomasulo’s Algorithm Overview
Tomasulo’s Algorithm: Three stages
Issue: Instructions fetched are issued to Reservation Stations (RS)
  If operands ready  Issue immediately
  If operands not ready  stall and wait for CDB
Execute: When all operands available, instruction executes
  Reservation Stations snoop CDB for missing operands
  When both operands ready, send to functional unit
Write Result: Broadcast on CDB
  All RS listen for their operands
  ROB marks instruction done
  Instruction commits in order
Notes: Tomasulo's Algorithm has three stages. Let me break down each one simply.
Stage 1: ISSUE
An instruction comes in. We check: are both operands ready right now? If yes, send it to the Reservation Station immediately with both values. If no — if one operand is still being computed — send it to the RS anyway, but without that operand. The RS will wait for it.
Stage 2: EXECUTE
The instruction sits in the RS waiting. Meanwhile, other instructions are finishing their execution. Their results broadcast on the CDB — the Common Data Bus.
The RS watches the CDB. When a result appears that it's waiting for, it grabs it. Once both operands are there, the instruction executes right away.
This is the magic: different instructions get their operands at different times. So they execute at different times. Out of order.
Stage 3: WRITE RESULT
The instruction finishes. The result broadcasts on the CDB with a tag that says which instruction it's for. The ROB marks that instruction as done. And when it's that instruction's turn in program order, the result gets written to the register file.
That's it. Three stages. The key is the RS and CDB working together — they let instructions execute whenever they're ready, not in order.

## Slide 5: System Architecture/Block Diagram
Data Flow: IQ RAT RS ALU/MEM  CDB  ROB RF
Notes: Here’s how the 8 components connect. Instructions enter through the Instruction Queue, get named in the RAT, scheduled in Reservation Stations, executed in functional units, result broadcast on CDB, and finally committed in order by the ROB.
The magic happens in three places: RAT for register renaming, RS for dynamic scheduling, and ROB for in-order commitment.

## Slide 6: Key components – The Big three
Three Critical Components:
RAT (Register Alias Table)
  Maps x0 to x31 to ROB entries
  Eliminates WAR/WAW hazards
  Enables out-of-order execution
RS (Reservation Stations)
  Buffers instructions and operands
  Watches CDB for operands
  Issue when ready (not in program order)
  This is where OOO happens
ROB (Reorder Buffer)
  Tracks all in-flight instructions
  Commits in program order
  This is why it’s safe to go out-of-order
Notes: Three components make Tomasulo work. Let me explain each one simply.
RAT — Register Alias Table
Here's the problem: two instructions both write to register x1. That's a conflict. The RAT solves it by renaming.
When instruction 1 writes to x1, the RAT says 'you're actually writing to ROB slot 3.' When instruction 2 writes to x1, it says 'you're writing to ROB slot 5.' Now they don't conflict. Different slots, no problem.
Why does this matter? Because now both instructions can execute in parallel without stepping on each other. The RAT eliminates false dependencies.
Reservation Stations — RS
The RS is a waiting room for instructions. When an instruction arrives and one operand isn't ready, it waits here.
But while it's waiting, other instructions can keep moving. The RS watches the CDB — the result bus. When a result it needs appears, it grabs it.
Once it has both operands, it executes immediately. No waiting in line. No program order. Whichever instruction is ready goes first. This is where out-of-order execution actually happens.
ROB — Reorder Buffer
The ROB is the safety net. Even though instructions execute out of order, the ROB makes sure they commit in order.
Instructions enter in order: slot 1, slot 2, slot 3. They execute at different times. But they commit in order — slot 1 first, then slot 2, then slot 3. Results go to the register file in program order.
This is why it's safe. The processor looks like it executed sequentially to the outside world. But internally, we got the speed of out-of-order execution.
That's the magic: RAT removes conflicts, RS executes dynamically, ROB commits safely

## Slide 7: RF - Register File
Key Observations:
x1 and x2 written simultaneously (40-80ns)
Values read correctly (100 – 120ns)
x0 always returns zero (protected)
Notes: The register file is the foundation. It has dual-port capability, two simultaneous writes and reads. This is essential for issuing instructions with two operands in parallel.
"This is the Register File simulation. The Register File is basically the processor's memory for temporary storage. Each register holds a 32-bit value.
Look at the waveform. You see WriteReg1_TB and WriteReg2_TB — these specify which registers we're writing to. At 40ns, we write to register x1. At 60ns, we write to register x2. Notice they're happening at the same time — that's the dual-port capability. Two writes in parallel.
Then look at WriteData1_TB and WriteData2_TB — these are the values being written. You can see they change as we write to different registers.
Finally, ReadReg1_TB and ReadReg2_TB show reads happening around 100-120ns. The read data comes back correctly.
Why does this matter? Because when we issue two instructions simultaneously, they both need to read their operands at the same time. The dual-port read capability makes that possible."

## Slide 8: Rat – Register alias table
Key Observations:
x1 ROB3(tag 0011)
x2 ROB5(tag 0101)
Reads return the ROB tags
Notes: The RAT maps registers to in-flight ROB entries. This is register renaming. Now when instruction 1 writes x1, and instruction 3 also writes x1, there’s no conflict they get different ROB entries.
"This is the Register Alias Table — the RAT. The RAT is the key to register renaming.
Think of it like a mapping table. When an instruction writes to a register, the RAT says 'Okay, x1 is now being written by ROB entry 0011.' When another instruction writes to x1, the RAT updates: 'x1 is now being written by ROB entry 0101.' No conflict.
Look at WriteRegister_TB[4:0] — that's the register being written (x0, x1, x2, etc.). Look at WriteTag_TB[3:0] — that's the ROB entry number.
At 20ns, we write x1 with tag 0000. At 40ns, we write x1 again with tag 0001. The RAT tracks both. Now when instruction 1 reads x1, it gets ROB entry 0000. When instruction 2 reads x1, it gets ROB entry 0001. Different ROB entries, no conflict.
This is register renaming. It eliminates false data dependencies and lets instructions execute out of order without conflicts."

## Slide 9: RS - Reservation stations
Key Observations:
Instruction with both operands execute immediately
Instruction with missing operand waits
CDB broadcasts operands at 80ns
Waiting instruction becomes ready and executes
Notes: Here’s when out-of-order execution actually happens. The second instruction has to wait for an operand, but the third instruction doesn’t. The third can execute first. RS watches the CDB, and as soon as its operand appears its ready to go.
The Reservation Station is where instructions wait for their operands and where out-of-order execution happens.
Look at issueTag_TB[3:0] — that's which instruction is being issued. You see tags 0000, 0001, 0010, 0011 — four different instructions.
Now look at issueSrc1Val_TB and issueSrc2Val_TB — these are the operand values. Some show actual values, some show zeros because the operands aren't ready yet.
Watch cdbValid_TB and cdbTag_TB — the CDB is broadcasting results. When a result appears on the CDB, the RS snoops it. Look at executeSrc1Val_TB and executeSrc2Val_TB — these start as zeros, but when the CDB broadcasts (around 100ns), they get filled in.
Finally, executeReady_TB goes high when both operands are ready. That's when the instruction can execute.
The magic here: instruction 1 might execute, then instruction 3 executes before instruction 2, because instruction 3's operands became ready first. That's out-of-order execution. The RS doesn't care about program order — it only cares about operand readiness

## Slide 10: ROB – Reorder buffer
Key Observations:
Three instructions enqueue
Results come in on CDB
Instructions commit in order (sequential)
ROB full detection works
Notes: Even thugh instructions might execute out of order, the ROB commits them in the original program order. This is the safety mechanism. The processor looks like it executed sequentially to the outside world.
This is the Reorder Buffer — the ROB. The ROB is the safety mechanism that makes out-of-order execution safe.
Look at enqueueDestinationReg_TB[4:0] — different instructions writing to different registers (x1, x2, x3, x4, etc.). They enqueue into the ROB one by one.
Now look at cdbValid_TB and cdbTag_TB — when the CDB broadcasts a result, it includes a tag that says 'This result is for ROB entry 0001.' The ROB marks that entry done.
Here's the key: look at commitDestinationReg_TB[4:0] and commitResult_TB[31:0]. commitEnable_TB goes high in sequence: at one time, instruction to x1 commits. Then instruction to x2. Then instruction to x3. In program order.
Even though the instructions might have executed out of order (CDB broadcasts happening at different times), the ROB makes sure they commit in order. Instruction 1 commits first, then instruction 2, then instruction 3.
This is why it's safe to go out-of-order. The ROB ensures the processor behaves as if instructions executed sequentially. To the outside world, everything looks correct.

## Slide 11: VHDL Implementation – code snippets
Key Observations:
Complete pipeline ADDI, LW, ADD
cdbValid pulses at different times (out-of-order execution)
commitEnable pulses sequentially (in-order commitment)
Notes: This is the complete pipeline executing three instructions: ADDI, LW, and ADD. Let me walk you through what's happening.
First, look at instructionInput_TB — you see three different instruction values being fed in at different times. That's ADDI, then LW, then ADD.
Now watch the key signals: cdbValid and cdbTag. Notice that cdbValid pulses (goes high) at different times — around 80ns, then 120ns, then 180ns. That means different instructions are finishing execution at different times. That's out-of-order execution.
But here's the magic: look at commitEnable — it pulses sequentially. One pulse, then the next, then the next. And cdbTag shows the sequence: 0000, then 0100, then 0000. The instructions commit in program order, even though they executed out of order.
This is Tomasulo's Algorithm working. Instructions execute whenever their operands are ready, not in program order. But they commit to the register file in program order, maintaining correctness. That's why it's safe, and that's why it's fast."

## Slide 12: Thank you
GitHub Link: https://github.com/Antwann03/RISC-V-OOO-Processor-with-Tomasulos-Algorithm
  Has the following paper, presentation, archived project, and zoom recording video link in a text file.